FlightKit

Flight
Logger

v1.0-0

Please note that this equipment is still under development. The developers do not accept any responsibility for loss or damage caused while using this device. Proceed with caution and test all functions thouroughly before actually using this with a model aircraft.

# Description
Flight logger allows a pilot to accurately record the aircraft's position, IMU data and 6 channels of control input. It also records the battery voltage and (optionally) the RSSI signal from the reciever. It can be used either as a stand-alone board, or in conjunction with a small reciever as a complete package.

The board measures 60mm by 30mm.
# Hardware Facilities
- LCD Display port
- Supports LCD displays with serial over I2C interfaces. The software is designed to work with a 20x4 Display.
- The LCD is intended to be plugged in as needed, not to be a permanant feature (of course, if you've got a big enough model...
- Servo PWM input (6 chans)
- Reads the position of 6 servo channels for later correlation with flight data.
- Micro SD card
- Storage for logged data
- Native USB (device port only)
- For programming over USB
- Serial expansion port (3.3v)
- This interface could be used for a live telemetry feed from the model.
- GPS
- The VENUS-638 is a 20Hz GPS unit.
- It needs an antenna for proper operation.
- IMU
- 16-bit measurement accuracy with a selection of ranges.
- Accelerations in X, Y and Z directions.
- Angular rates about X,Y and Z axes.
- Magnetometer readings in X,Y and Z directions.
- All via a single MPU9150 chip.
- Analogue I/O capability
- Two analogue channels are used to read battery voltage and RSSI.
- The RSSI line can be used to read another value in the range 0V-3.3V, if RSSI is not needed or not available.
- Digital I/O capability
- Provision for 4 digital inputs or outputs.
- These lines are intended for switch inputs.
- They connect directly to the MPU.
- Extra circuitry will be required to use them as outputs.

# Connector Details

Port	Purpose
P101	Battery power input
P102	Servo input channels
P103	LCD Interface header
P104	Serial expansion header
P105	Digital IO header
JP201	Software erase jumper
P401	GPS Antenna port
USB	Native USB port
MicroSD	Slot for storage card

# Data logging settings format